## Slide 1
ADAS – Advanced Driver Assistance System
Camera-Only Modular System for Indian Road Conditions
Real-Time • Edge-Deployable • YOLOv8 + DeepSORT • Python
System Architecture & Technical Workflow

## Slide 2
Agenda
01
System Overview & Architecture
02
Tech Stack
03
Module 1: Forward Collision Warning
04
FCW: Traffic-Aware Thresholds
05
Module 2: Lane Assist + Blind Spot
06
Module 3: Emergency Vehicle Preemption
07
Shared Infrastructure
08
Performance & Optimizations
09
Evaluation Framework
10
Future Roadmap

## Slide 3
System Overview
3 independent ADAS modules + shared infrastructure, optimized for Indian traffic
🚗 FCW
Forward Collision Warning
Detects vehicles ahead, estimates distance & TTC, warns before collision
Front Camera
🛣 BSD
Lane Assist + Blind Spot
Detects lane boundaries, identifies blind spot vehicles, advises lane changes
Rear Camera
🚨 EVP
Emergency Preemption
Detects emergency vehicles via flashing lights + siren audio, advises yielding
Front + Mic
Each module runs independently • Video or live camera • Batch launcher included

## Slide 4
Technology Stack
Object Detection
YOLOv8n (Ultralytics)
6.5MB, 80 COCO classes, FP16 + TensorRT
Object Tracking
DeepSORT + MobileNet
Kalman filter + cosine re-identification
Computer Vision
OpenCV 4.8+
BEV transforms, Hough lines, HSV masks
Math / Signals
NumPy + SciPy
Polynomial fitting, FFT audio analysis
GPU Acceleration
PyTorch CUDA + FP16
Half-precision, TensorRT export
Audio (Optional)
PyAudio
Real-time mic for siren detection
Profiling
psutil + custom profiler
FPS, bandwidth, storage estimation

## Slide 5
Module 1: Forward Collision Warning (FCW)
Detects vehicles ahead in ego lane, estimates distance & closing speed, warns before collision
1
Frame 640×360
→
2
YOLOv8n Detect
→
3
DeepSORT Track
→
4
BEV Lane Detection
→
5
In-Lane Filter
→
6
Distance + TTC
→
7
Traffic Decision
Key Components:
▸ Lane Detection: Bird's-Eye-View transform + sliding window polynomial fitting
▸ Distance: Pinhole camera model d = (1.5m × 500px) / bbox_height
▸ TTC: closing_speed = (dist_prev − dist_curr) × FPS → TTC = dist / speed
▸ Traffic Context: Heavy (≥8 vehicles) thresholds ×0.5 to reduce false alarms
▸ Warning: 4 levels (Normal→Visual→Audio→Continuous), never skips levels

## Slide 6
FCW: Traffic-Aware TTC Thresholds
In heavy Indian traffic, vehicles are always close — adaptive thresholds prevent false alarms
Traffic Level
Vehicle Count
TTC Critical
TTC Warning
Multiplier
FREE
< 4
2.0s
4.0s
×1.0
MODERATE
4 – 7
1.4s
2.8s
×0.7
HEAVY
≥ 8
1.0s
2.0s
×0.5
FCW Source Files:
main.py – Pipeline | collision.py – TTC + Distance | lane_detector.py – BEV Sliding Window
ego_path.py – Ego path overlap | motion_metrics.py – EMA smoothing | traffic_engine.py – Density
warning_manager.py – 4-level state machine | lane_analyzer.py – Legacy Hough detector

## Slide 7
Module 2: Lane Assist + Blind Spot Detection
Rear camera: lane boundary analysis + blind spot 3D cube zones + lane change advisory
Blind Spot Detection Pipeline
1. BEV perspective transform (rear trapezoid → rectangle)
2. HSV thresholding: white + yellow lane markings
3. Morphological cleanup (close + open, 5×5 kernel)
4. Sliding window → 2nd-degree polynomial lane fitting
5. History smoothing (average over 10 frames)
6. Generate 3D blind spot cubes (140px wide)
7. Inverse transform cubes back to camera view
Lane Change Advisory States
SAFE_BOTH
Both sides clear
SAFE_LEFT / RIGHT
One side clear
UNSAFE_LEFT / RIGHT
Vehicle in blind spot
UNSAFE_BOTH
Stay in lane!
NO_DATA
Insufficient lane data
Critical: drifting >0.3m toward occupied blind spot → "DON'T MOVE LEFT/RIGHT!"

## Slide 8
Module 3: Emergency Vehicle Preemption (EVP)
Visual Detection
HSV color detection in top 30% of each vehicle bbox:
Red: [0,120,150]–[10,255,255] (Ambulance, Fire)
Blue: [100,120,150]–[130,255,255] (Police)
Amber: [10,100,200]–[25,255,255] (Highway patrol)
Contour area: 100px² ≤ area ≤ 5000px²
Blink frequency: 1.0–4.0 Hz = emergency vehicle
Blinking = 0.9 confidence; Static = 0.5
Audio Siren Detection
FFT on mic audio (22050 Hz, 2048 chunks)
Indian siren band: 600–1600 Hz
Ratio = siren_energy / total_energy
Warble pattern: variance > 0.001
Graceful fallback if PyAudio absent
Multi-Modal Fusion
fused = max(visual, audio)
Both > 0.3: vis×0.6 + aud×0.4 + 0.2 (boost)
NORMAL → ALERT (5f) → YIELD (10f)
Never jumps NORMAL → YIELD
Direction: LEFT / RIGHT / BEHIND

## Slide 9
Shared Infrastructure
detector.py
YOLOv8n Wrapper
FP16 on GPU
TensorRT .engine support
Model warmup
ROI cropping
5 vehicle classes
tracker.py
DeepSORT Tracker
MobileNet embedder
Kalman prediction
Cosine re-ID
10-frame history
Speed estimation
ui_renderer.py
HUD UI Renderer
Dark transparent panels
Green/Amber/Red colors
Corner-accent boxes
Gradient alert banners
Dashboard composer
profiler.py
Module Profiler
Per-frame timing
JPEG data estimation
Bandwidth (KB/s)
Storage (MB/hour)
CSV export

## Slide 10
Performance & Optimizations
≥ 15 FPS
Target Rate
640×360
Resolution
6.5 MB
Model Size
< 67ms
Latency (GPU)
Every 2nd
Det Interval
Optimization Techniques
▸ FP16 Half-Precision: 2× faster inference on NVIDIA GPUs
▸ TensorRT Export: .engine format for 2-3× speedup
▸ Frame Skipping: YOLO every 2nd frame, tracker predicts between
▸ ROI Cropping: Crop irrelevant regions (BSD: skip top 20%)
▸ Model Warmup: Pre-warm to avoid startup latency
▸ History Smoothing: EMA + rolling averages for stability

## Slide 11
Evaluation Framework
Interactive annotation tool (evaluate.py) for measuring detection quality
▸ Samples N evenly-spaced frames from video (default: 200)
▸ Runs module pipeline and displays result for annotation
▸ Human classifies: TP / FP / FN / TN per frame
▸ Computes: Precision, Recall, F1 Score, Accuracy
▸ Exports to JSON + CSV for reports
▸ Supports: lane, lane_fcw, bsd, fcw modules
Commands:
python evaluate.py --module lane --source videos/new.mp4
python evaluate.py --module bsd --source videos/new.mp4
python evaluate.py --module fcw --source videos/new1.mp4

## Slide 12
Future Roadmap
Area
Current
Proposed
Lane Detection
BEV sliding window
Ultra-Fast-Lane DNN
Distance
Pinhole camera
MiDaS/ZoeDepth
Multi-Module
Independent exec
Unified pipeline
Siren
FFT energy
Mel-spectrogram + CNN
Night Mode
Fixed thresholds
Adaptive + IR camera
Edge Deploy
Python + PyTorch
ONNX → TensorRT

## Slide 13
Thank You
ADAS – Camera-Only Modular System for Indian Roads
Questions & Discussion