## Slide 1
Unified ADAS Pipeline
Tri-Staggered Dual-AI Architecture for Indian Roads
FCW B7 Blind Spot B7 Emergency Preemption B7 Dynamic Skipping
Monthly Committee Technical Update

## Slide 2
Agenda
01
The True Dual-Model Unified Pipeline Architecture
02
Core Optimizations: Tri-Staggered Execution & Dynamic Skipping
03
Module 1: Context-Aware Forward Collision Warning (FCW)
04
Module 2: Lane Assist & Blind Spot Analytics (Rear)
05
Module 3: Multi-Modal Emergency Preemption (EVP)
06
Advanced Tracking & HUD Rendering
07
Profiling & Metrics (unified_profile.csv)

## Slide 3
True Dual-Model Unified Pipeline
Previously isolated modules are now unified. Processes Front & Rear cameras simultaneously.
General Traffic AI
yolov8n.pt
Detects Cars, Trucks, Pedestrians, Bikes on Front + Rear cameras.
Emergency Veh. AI
yolo_emergency_model.pt
Specialized model dedicated to Ambulances, Fire Trucks, Police.
DeepSORT Trackers
3 Independent Streams
Separate trackers for Front, Rear, and EVP streams ensuring no mixups.

## Slide 4
Optimizations: Tri-Staggered Exec & Dynamic Skip
Massive CPU/GPU savings achieved by intelligently staggering workloads and skipping empty frames.
Tri-Staggered Detection Rate (Interval = 3):
B7 Frame N+0: Front Camera AI Inference
B7 Frame N+1: Rear Camera AI Inference
B7 Frame N+2: Emergency Camera AI Inference
Result: Avoids running 3 heavy models on the same frame, eliminating latency spikes.
Dynamic Empty-Road Skipping:
B7 If the system detects 0 vehicles for 2 consecutive runs (6 frames)...
B7 It safely assumes an empty road and forces skips for the next 6 frames.
B7 DeepSORT Coasting keeps existing objects alive seamlessly.
Result: Drastically cuts CPU usage during open highway driving or stopped traffic.

## Slide 5
Module 1: Context-Aware FCW
Uses 'get_ego_polygon' logic instead of simple bounding box overlaps.
B7 Ego Path Polygon: Defines a 45% width, 65% height corridor ahead of the driver.
B7 Context Validation: Targets must have >25% horizontal overlap with this polygon.
B7 Traffic-Aware TTC Thresholds:
- FREE (< 4 vehicles): Warns at 4.0s, Critical at 2.0s.
- HEAVY (>= 8 vehicles): Warns at 2.0s, Critical at 1.0s (avoids false alarms in jams).
B7 DeepSORT Speeds: Closing speed derived from tracking bounding box growth.
B7 Pedestrian Alert: Special DANGER overlay if a pedestrian (Class 0) enters Ego Path.

## Slide 6
Module 2: Lane Assist & Blind Spot
Rear Camera Analytics: Lane Advisory, 3D Cubes, ROI Cropping.
B7 ROI Cropping: Top 20% of rear frame is cropped to save processing time.
B7 3D Blind Spot Cubes: Projects a polygon to the left/right of detected lanes.
B7 Intersection Testing: If a vehicle bounding box footprint hits the cube = In Blind Spot.
B7 Lane Change Advisor: Evaluates both lanes simultaneously.
B7 Outputs 'UNSAFE_LEFT', 'UNSAFE_RIGHT', 'SAFE_BOTH', triggering an Amber Alert if driver signals.

## Slide 7
Module 3: Multi-Modal EVP
Emergency Vehicle Preemption: Identifies active emergency scenarios securely.
Visual Detection
HSV detection for Red, Blue, Amber.
Blink frequency verification (1-4Hz).
Scans only the top 30% of Emergency Bboxes.
Audio Siren (Optional)
FFT Analysis over Indian Siren Band (600-1600Hz).
Calculates Warble variance.
Graceful degradation if no Mic.
Multi-Modal Fusion
fused = max(visual, audio).
If both > 0.3, boosts confidence.
10 frames to reach state 'YIELD'.

## Slide 8
HUD Rendering & Performance Profiling
HUD UIRenderer:
B7 Semi-transparent panels with Corner-Accent glowing bounding boxes.
B7 Dynamic Dashboards for Front (FCW/EVP) and Rear (BSD/Lane offset).
B7 Full-screen Red Alert 'PEDESTRIAN IN PATH!' override when needed.
Metrics & Logging (ModuleProfiler):
B7 Measures accurate FPS, Time per frame, data bandwidth.
B7 Logs states directly to unified_profile.csv and evp_profile.csv.
B7 Ensures real-time evaluation capability to catch bottlenecks in edge deployments.

## Slide 9
System Ready for Edge Deployment
Unified Pipeline B7 Tri-Staggered AI B7 Context-Aware FCW
Questions & Discussion